## Slide 1: Final Project
Raikes 284H

## Slide 2: Components You’ll Need …
Program Counter (8-bit counter)
Instruction Register
Decoder (VHDL please)
Register File (need a demux)
RAM & ROM (use Altera’s library)
ALU + Shifter
Synchronizing clock
Clock (1 Hz for debugging, provided)

## Slide 3: Program Counter
N-bit counter that counts up each time a clock arrives (8count is available in Altera library)
  N is set to the maximum address for your ROM
  Must have a clock input
  Must have target_address input to support branching
    Must have a write enable to control when to write the new address (write when 1, count up when 0)

## Slide 4: Instruction Register (Optional)
Hold the current instruction while the Program Counter (PC) increments to the next instruction

## Slide 5: Register File
Contains a collection of registers
  Must support write to a particular register (1 write port)
    Clock and write enable are needed
  Must support read from a particular register (2 read ports)

## Slide 6: RAM
Used to hold data
  you can adjust the configuration based on your need (e.g., change LPM_WIDTH to 16 to store 16-bit data)

## Slide 7: ROM
Used to hold binary program
  Configuration should be changed according to your need

## Slide 8: ALU + Shifter
ALU: Performs the basic operations including add, subtract, and, or
  Ripple carry adder can be used (from your lab)
  Support zero output
  Support overflow detection
Shifter: Performs multiple bits shifting

## Slide 9: Synchronizing Clock
One potential way to synchronize the operation is to create a synchronizing clock
  Takes a clock input
  Outputs two (or three) clock signals
clock |  |  |  |  |  |  |  |  |  |  |  |  | 
clock0 |  |  |  |  |  |  |  |  |  |  |  |  | 
clock1 |  |  |  |  |  |  |  |  |  |  |  |  | 
clock2 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: Synchronizing Clock
How many devices need clock signals to operate?
  IR (if you choose) (clock 0?)
  RAM (clock 1?)
  Register file (clock 1?)
  PC (clock2?)

## Slide 11: Helpful Advices
Agree on a convention
  When declare a bus, choose a consistent definition of bus width (a[7..0] or a[0..7])
    Inconsistency is a major headache
    Typically, a[7..0] is used (7 is msb and 0 is lsb)
Don’t throw in everything all at once
  Test each component thoroughly
  Step wise refinement
    Connect PC to ROM then test
    Add IR then test again
Think about front-end/back-end
  Front end might include PC/ROM/IR/sync_Clock
  Backend might include decoder, RF, ALU/shifter, RAM
Think about how to debug
  Add hardware components to connect to switches and displays (check RF contents)